## Slide 1: ロボット経由点軌道探索: 深層強化学習の実装と迷路問題での評価
AI研究部
AIエンベデット研究室
AIエンベデット１課 張家銓
2018.11.02
Notes: 今回報告のタイトルはロボット経由点軌道探索:深層強化学習の実装と迷路問題での評価です。

## Slide 2: 1. Timeline 2. Background 3. Deep Reinforcement Learning 4. Conclusion 5. Future Works
Outline
Notes: 今回報告のoutlineはは御覧の通り、次から次へと紹介します

## Slide 3: 1. Timeline 2. Background 3. Deep Reinforcement Learning 4. Conclusion 5. Future Works
Outline
Notes: 最初はtimelineについて、私は配属された以来、この兩月の間やったの事を簡単に説明します

## Slide 4: Timeline
2019
Apply several methods to improve performance
9月
4月
10月
Arrive Japan
Settle down
In 先端研
Build
Environment
(New PC, Linux OS, Tensorflow, Keras …)
-Start to implement Maze and DQN
Read papers, debug and discuss
Notes: 私は九月から先端研に配属されました、最初は

## Slide 5: 1. Timeline 2. Background 3. Deep Reinforcement Learning 4. Conclusion 5. Future Works
Outline

## Slide 6: Background
Robot motion planning in complex environment
(Provided by Denso Wave)
-Complex environment
・Several obstacles in motion plan
・Several checkpoint for robot arm
-Motion planning
Find out the optimal solution
・Path, posture, trajectories, controlling values…
・Collision-free
Production process layout

## Slide 7: Background
Chart: 
都市数
ルート数
約6秒(※1)
約1401万年(※1)
階層3(移動)
階層1(手順)
階層2(経由点)
100x100x100⇒1.0×1011
6関節⇒2.0×1017
都市数20⇒1.2×1018
都市数30⇒1.3×1032
手順探索 (階層1)
経由点探索 (階層2)
2点間移動 (階層3)
対象タスク：ロボット組立問題
J1： +/- 180°
J2： +120°, -115°
J3： +141°, -115°
J4： +/- 270°
J5： +/- 115°
J6： +/- 360°
巡回ｾｰﾙｽﾏﾝ問題
パスプランニング
ロボット制御
※1 スーパーコンピュータ京
各階層単体でも膨大な探索空間であるため、探索を効率良く行う枠組み(※)が必要である
※各階層ごとに最適化を図り、それにより全体での最適化も図られる手法を検討する
ウェーブ要求スペック：
①部品数10～100(階層1)
②空間サイズ1~3cm間隔(階層2)
②安定した収束(階層1,2,3)
高次元化への対応

## Slide 8: 1. Timeline 2. Background 3. Deep Reinforcement Learning -Apply on Maze solving -Compare with tree search algorithms -Improvement 4. Conclusion 5. Future Works
Outline

## Slide 9: Deep Reinforcement Learning
Apply DQN on Maze solving problem:
Current State
Game play
DB
Neural Network
Add
Left:0.5
Down:0.3
Right:0.1
Up:-0.1
Random Fetch and Update weights
Max Q
Make move
Q value

## Slide 10: DQN - maze solving
10x10 Maze: win rate 100%
-Training time: <1 hours
40x40 Maze: win rate 98%
-Training time: ~1.5 days
Chart: 

## Slide 11: DQN – compare with tree search algorithms
Compare with basic tree search algorithms:
-Depth first search : Stuck when size > 15x15
-Breadth first search: (Optimal guaranteed) : Stuck when size > 20x20
-A* (Optimal guaranteed) : Stuck when size > 35x35
Advanced search algorithms for robot motion planning
-HD*
-RRT
-…
40x40 Maze

## Slide 12: DQN - Improvement
Issue:
-Reduce input Size
-Improve the performance
-Reduce training time
-Path Optimization

## Slide 13: DQN - Improvement
1.Reduce Input State Size
-Current input state:
-Global visited map -> Local Visited map
Current pos
Goal pos
Global
visited map
+
+
Global
visited map
Local
visited map
Win rate stuck in ~30% in 40x40 maze

## Slide 14: DQN - Improvement
2.Improve the performance
Double DQN
Duel DQN
Win rate:~94%
Win rate:~60%

## Slide 15: DQN - Improvement
3.Reduce Training time
Network structure:
Fully-connected
1.Breadth
2.Depth
Convolutional
1.Normal CNN
2.Recidual CNN
Input
FC Layer
Output
Input
FC Layer
Output
…
FC Layer
4800(Nueron) x 1(Layer)
600(Nueron) x 8(Layer)
Win rate:~98%
Win rate:~50%
Win rate:~40%
Win rate:~60%
May require more computation Resource

## Slide 16: DQN - Improvement
4.Path Optimization
1. Give penalty when change the direction
2. Add optimal solutions into transition data base
Ongoing:

## Slide 17: 1. Schedule 2. Background 3. Deep Reinforcement Learning 4. Conclusion 5. Future Works
Outline

## Slide 18: Conclusion and Future works
Conclusion
-Apply deep reinforcement learning on maze solving problem
-Achieve win rate 100% in 10x10 , 98% in 40x40 Maze
-Apply several methods to improve performance
Future Works
-Apply it on 3D Maze (60x60x40…)
-Make problems more realistic:
-Consider type and pose of the robots
-Try different methods to improve performance and speed
-Asynchronous Advantage Actor-Critic (A3C)
-Value Network + Policy Network
…

## Slide 20: テーマの概要
複雑環境下での行動計画
（ウェーブとの共有テーマ）
⇒ これまで人手でやっていたことを強化学習で実現
(プログラムレス化)
要素技術開発実験の様子
ー複雑環境
・ロボットの行動空間に障害物が存在する
・取り扱う部品や作業位置が複数個所存在する
ー行動計画
作業時間を最短化する行動の生成
・最適な作業手順の決定
・最適な軌道・姿勢・制御値の決定
・衝突回避
作業レイアウトの一例

## Slide 21: 研究課題
Chart: 
都市数
ルート数
約6秒(※1)
約1401万年(※1)
階層3(移動)
階層1(手順)
階層2(経由点)
100x100x100⇒1.0×1011
6関節⇒2.0×1017
都市数20⇒1.2×1018
都市数30⇒1.3×1032
手順探索 (階層1)
経由点探索 (階層2)
2点間移動 (階層3)
対象タスク：ロボット組立問題
J1： +/- 180°
J2： +120°, -115°
J3： +141°, -115°
J4： +/- 270°
J5： +/- 115°
J6： +/- 360°
巡回ｾｰﾙｽﾏﾝ問題
パスプランニング
ロボット制御
※1 スーパーコンピュータ京
各階層単体でも膨大な探索空間であるため、探索を効率良く行う枠組み(※)が必要である
※各階層ごとに最適化を図り、それにより全体での最適化も図られる手法を検討する
前回報告済み
本日報告(劉T)
本日報告(蓑谷T)
ウェーブ要求スペック：
①部品数10～100(階層1)
②空間サイズ1~3cm間隔(階層2)
②安定した収束(階層1,2,3)
高次元化への対応